## Slide 1
Emerging Technologies for the Circular Economy
Lecture 5b: IoT Security and Privacy
Prof. Dr. Benjamin Leiding (Clausthal)
M.Sc. Arne Bochem (Göttingen)
M.Sc. Anant Sujatanagarjuna (Clausthal)
Notes: <number>

## Slide 2
License
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License. To view a copy of this license, please refer to https://creativecommons.org/licenses/by-sa/4.0/ .
Updated versions of these slides will be available in our Github repository.

## Slide 3
Examples and Lessons Learned

## Slide 4
Who Refuses to Wash Hands?

## Slide 5
Who Refuses to Wash Hands?
Swagatam Majumdar – https://commons.wikimedia.org/wiki/File:How_PIR_Sensor_Device_Detects_Human_Presence.gif – CC BY-SA 4.0

## Slide 6
Who Refuses to Wash Hands?

## Slide 7
Who Refuses to Wash Hands?
Lessons learned:
  Correlation of data might reveal interesting and unexpected information.
  Implement existing IT security and data protection concepts (KNX can be operated securely) → e.g. encryption and authentication.
  In general:
    Collect/store/analyze data vs. GDPR
    Stored data must be secured and protected accordingly

## Slide 8
Jeep Cherokee Hack 2015
EurovisionNim – https://commons.wikimedia.org/wiki/File:2015_Jeep_Cherokee_(KL)_Longitude_wagon_(2018-09-03)_01.jpg – CC BY-SA 4.0

## Slide 9
Jeep Cherokee Hack 2015
https://www.kaspersky.com/blog/blackhat-jeep-cherokee-hack-explained/9493/

## Slide 10
Jeep Cherokee Hack 2015
https://www.kaspersky.com/blog/blackhat-jeep-cherokee-hack-explained/9493/
  WPA2 password → “TyYMxfPhZxkp”
This corresponds to Epoch time 0x50e22720
This is Jan 01 2013 00:00:32 GMT
Took 32 seconds for WifiSvc to get started up
Really only a few dozen passwords to try

## Slide 11
Jeep Cherokee Hack 2015
https://www.kaspersky.com/blog/blackhat-jeep-cherokee-hack-explained/9493/
  WPA2 password → “TyYMxfPhZxkp”
  This corresponds to Epoch time 0x50e22720
This is Jan 01 2013 00:00:32 GMT
Took 32 seconds for WifiSvc to get started up
Really only a few dozen passwords to try

## Slide 12
Jeep Cherokee Hack 2015
https://www.kaspersky.com/blog/blackhat-jeep-cherokee-hack-explained/9493/
  WPA2 password → “TyYMxfPhZxkp”
  This corresponds to Epoch time 0x50e22720
  This is Jan 01 2013 00:00:32 GMT
Took 32 seconds for WifiSvc to get started up
Really only a few dozen passwords to try

## Slide 13
Jeep Cherokee Hack 2015
https://www.kaspersky.com/blog/blackhat-jeep-cherokee-hack-explained/9493/
  WPA2 password → “TyYMxfPhZxkp”
  This corresponds to Epoch time 0x50e22720
  This is Jan 01 2013 00:00:32 GMT
  Took 32 seconds for WifiSvc to get started up
  Really only a few dozen passwords to try

## Slide 14
Jeep Cherokee Hack 2015
Lessons learned:
  No security by obscurity

## Slide 15
More examples

## Slide 16
Fish Tank Thermometer
  Casino with fish tank in the lobby
  IoT fish tank thermometer
  Attackers compromise thermometer
  Use it to further compromise local network
  Exfiltrate customer database
https://www.businessinsider.in/Hackers-stole-a-casinos-high-roller-database-through-a-thermometer-in-the-lobby-fish-tank/articleshow/63769685.cms

## Slide 17
Fish Tank Thermometer
Lessons learned:
  IoT devices can be the weakest link
  Consider security between possibly vulnerable devices and local networks
https://www.businessinsider.in/Hackers-stole-a-casinos-high-roller-database-through-a-thermometer-in-the-lobby-fish-tank/articleshow/63769685.cms

## Slide 18
Library vulnerabilities: NAME:WRECK
  Vulnerabilities in multiple TCP/IP stacks
  Impact: From DoS to RCE
  Affects:
    Medical devices
    Avionics
    Baseband processors in mobile phones
    Servers
  Vulnerability in domain name parsing
https://www.forescout.com/company/resources/namewreck-breaking-and-fixing-dns-implementations/

## Slide 19
Ripple20
  19 vulnerabilities including remote code execution in widely used low-level TCP/IP-stack library distributed under various names
  “Affected vendors range from one-person boutique shops to Fortune 500 multinational corporations, including HP, Schneider Electric, Intel, Rockwell Automation, Caterpillar, Baxter, as well as many other major international vendors suspected of being of vulnerable in medical, transportation, industrial control, enterprise, energy (oil/gas), telecom, retail and commerce, and other industries.” – JSOF
  Demonstration: Turning off IoT UPS
https://www.jsof-tech.com/disclosures/ripple20/

## Slide 20
Library Vulnerabilities
Lessons learned:
  Even widely used libraries can contain grave security issues

## Slide 21
SECURING the IoT

## Slide 22
Security
General best practices for developing secure software
  Avoid common issues:
      Buffer overflows
      SQL injections
      etc..
  Input validation
  Secure defaults
  Overall system design
May also need to consider hardware security
  Tamper-proof devices
However: Often IoT devices are not designed with security in mind from the start.

## Slide 23
Cryptography (1)
Consider low-power devices
Common protocols (SSL/TLS) often too heavy
Main things to consider:
  Confidentiality
  Integrity
  Authentication
Different approaches

## Slide 24
Cryptography (2)
RSA too heavy for very low-powered devices
ECC can be acceptable, but still slow
Main focus on symmetric cryptography:
  AES128 can perform well even on 8bit micro-controllers
  Block cipher based MACs
  SipHash (but is short)
  SHA family comparatively slow
Issue: Shared keys
https://www.mdpi.com/1424-8220/15/8/19560/htm
O. Alfandi, A. Bochem, A. Kellner, C. Göge, D. Hogrefe (2015) – Secure and Authenticated Data Communication in Wireless Sensor Networks – https://www.mdpi.com/1424-8220/15/8/19560/htm – CC BY 4.0

## Slide 25
Privacy
Complex topic
Requires:
  Secure implementations
  Additional care take to:
      Minimize personal data being stored/processed
      Where possible, process locally
      Where necessary, store encrypted
      Trust considerations

## Slide 26
Questions?