## Slide 1
Emerging Technologies for the Circular Economy
Lecture 11: Blockchains and Sustainability
Prof. Dr. Benjamin Leiding (Clausthal)
Dr. Arne Bochem (Göttingen)
M.Sc. Anant Sujatanagarjuna (Clausthal)

## Slide 2
License
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License. To view a copy of this license, please refer to https://creativecommons.org/licenses/by-sa/4.0/ .
Updated versions of these slides will be available in our Github repository.

## Slide 3
Exam
There will be a pre-exam Q&A session before the exam
  Where: BBB → ETCE Q&A Room (Link)
  When: 31.07.23 - 14:15 - 15:30
Pre-Exam Q&A Session

## Slide 4
BLOCKCHAINS AND SUSTAINABILITY

## Slide 5
Two main perspectives
Sustainability of Blockchains
VS
Blockchains for Sustainability

## Slide 6
Sustainability of Blockchains
Elephant in the room → Proof Of Work (Bitcoin)

## Slide 7
Sustainability of Blockchains
Elephant in the room → Proof Of Work (Bitcoin)
Network | Annual Energy Consumption (TWh) | Market Capitalization ($ Billion) | Energy Consumed per Transaction (kWh/tx)
Visa | 197.57 (2021) [2] | 520.62 (2021) [2] | 0.0015 (2021) [2]
Bitcoin | 135.12 (2021) [2] | 617.05 (2021) [2] | 1777.11 (2021) [2]
Ethereum (PoW) | 55.01 (2021) [2] | 247.8 (2021) [2] | 125.36 (2021) [2]
Ethereum (PoS) | 0.0026* (2022) | 222.9 (today) | Can be anywhere between 0.00009 and 0.55713 [1]
https://ethereum.org/en/energy-consumption/
[2] Varun Kohli, Sombuddha Chakravarty, Vinay Chamola, Kuldip Singh Sangwan, Sherali Zeadally, An analysis of energy consumption and carbon footprints of cryptocurrencies and possible solutions, Digital Communications and Networks, Volume 9, Issue 1, 2023, Pages 79-89, ISSN 2352-8648, https://doi.org/10.1016/j.dcan.2022.06.017
https://coinmarketcap.com/currencies/ethereum/
[1] Platt, Moritz, et al. "The energy footprint of blockchain consensus mechanisms beyond proof-of-work." 2021 IEEE 21st International Conference on Software Quality, Reliability and Security Companion (QRS-C). IEEE, 2021.

## Slide 8
Sustainability of Blockchains
The potential utility of blockchains in solving issues and making the world more sustainable, far overweighs the disadvantages of early concensus mechanisms.
Circular Economy models are designed to decouple resource consumption and economic growth.
Decoupling Resource Consumption and Potential Utility

## Slide 9
Sustainability of Blockchains
The utility of blockchains in solving issues and making the world more sustainable, far overweighs the potential disadvantages of early concensus mechanisms.
Circular Economy models are designed to decouple resource consumption and economic growth.
→ For this lecture, we will try decouple resource consumption of blockchains and their potential utilty towards sustainabilty.
Decoupling Resource Consumption and Potential Utility

## Slide 10
BLOCKCHAINS FOR SUSTAINABILITY

## Slide 11
Blockchains for Sustainability
Which of the following properties of Blockchains would you value the most, when it comes to the potential utility for “making the world more sustainable / the economy more circular” ?
  Verifiability / Traceability / Transparency
  Decentralizing aspects (concensus)
  Immutability
  Security (e.g., preventing double-spending)
  (Psuedo-) Anonymity
Question

## Slide 12
Blockchains for Sustainability
Emmissions Trading
Sustainable Energy
Sustainable Mobility
Sustainable Supply-chain management
Example Use-Cases

## Slide 13
Blockchains for Sustainability
Emissions Trading
Sustainable Energy
Sustainable Mobility
Sustainable Supply-chain management
Example Use-Cases

## Slide 14
Emissions Trading
Quick Introduction
An approach to limit climate change by creating a market with limited allowances for emissions. (Cap and Trade)
Regulators set a quantitative total limit on the emissions produced by participating polluters (e.g., oil companies).
A polluter having more emissions than their assigned quota MUST purchase the right to emit more.
A polluter emitting fewer emissions than their assigned quota CAN sell their remainder to other polluters.
One of the most common policy adopted by countries to meet their pledges under the Paris Agreement.
https://en.wikipedia.org/wiki/Carbon_emission_trading

## Slide 15
Emissions Trading
EU-ETS
EU’s Emissions Trading System (EU-ETS):
  Currently covers ~45% of the EU’s emissions.
  Includes power producers, aviation industry and manufacturing.
  EU Commission proposed to include maritime emissions into the ETS in 2020.
“EUA prices in the EU-ETS until 2021-10” authored by Allavion is licensed under CC BY-SA 4.0 International
https://en.wikipedia.org/wiki/European_Union_Emissions_Trading_System

## Slide 16
Emissions Trading
EU-ETS: Problems and Criticisms
What about the remaining ~55%?
At least 10 differrent types of fraudulent activities are possible:
  Double counting
  Exploitation of weak regulations
  Tax fraud
Oversupply of emissions allowances
“EUA prices in the EU-ETS until 2021-10” authored by Allavion is licensed under CC BY-SA 4.0 International
Mandaroux, Rahel, Chuanwen Dong, and Guodong Li. 2021. "A European Emissions Trading System Powered by Distributed Ledger Technology: An Evaluation Framework" Sustainability 13, no. 4: 2106. https://doi.org/10.3390/su13042106
https://en.wikipedia.org/wiki/European_Union_Emissions_Trading_System

## Slide 17
Emissions Trading
EU-ETS on a Blockchain
Mandaroux, Rahel, Chuanwen Dong, and Guodong Li. 2021. "A European Emissions Trading System Powered by Distributed Ledger Technology: An Evaluation Framework" Sustainability 13, no. 4: 2106. https://doi.org/10.3390/su13042106
A conceptual idea for digitizing the EU-ETS in a decentralized and transparent way.
Installation holders (trading participants) use Decentralized Identifiers (DIDs) as an anchor to their identity.
Regulatory autorities assign allowances to the partners in the form of a digital certificate (Verifiable Credentials), which serve as the emissions certificate.
Installation holders have a unique wallet that represents their DID, emission credits, and auditable transaction history.
Smart contract connected smart meters, can further automate tracking of verified emissions.

## Slide 18
Emissions Trading
EU-ETS on a Blockchain
Mandaroux, Rahel, Chuanwen Dong, and Guodong Li. 2021. "A European Emissions Trading System Powered by Distributed Ledger Technology: An Evaluation Framework" Sustainability 13, no. 4: 2106. https://doi.org/10.3390/su13042106
Advantages:
  Double counting would be reduced due to more secure unique identification and trade tracking.
  With wallet information, each trade can be traced back to the original holder.
  Real-time energy data can influence allocation policies in a more efficient way.

## Slide 19
Emissions Trading
EU-ETS on a Blockchain
Mandaroux, Rahel, Chuanwen Dong, and Guodong Li. 2021. "A European Emissions Trading System Powered by Distributed Ledger Technology: An Evaluation Framework" Sustainability 13, no. 4: 2106. https://doi.org/10.3390/su13042106
Disadvantages
  A very generalized framework
  Does not address all types of fraudulent activities.
  Does not fix the ~55% of emissions that are not traded in the system.
  Adoption of digitization through blockchains regarding traceability and transaparency is still a general issue.

## Slide 20
Blockchains for Sustainability
Emissions Trading
Sustainable Energy
Sustainable Mobility
Sustainable Supply-chain management
Example Use-Cases

## Slide 21
Sustainable Energy
Example: NRGCoin
Incentivization of production and consumption of locally sourced renewable energy using a blockchain.
The protocol converts locally produced renewable energy to NRGCoins. (1 kWh = 1 NRGCoin)
NRGCoin can be exchanged for standard currencies at any time (€, $, …).
Producers do not rely on batteries, but continuously feed energy into the grid.
Payment (NRGCoin) is received based on actual usage, as consumption is monitored in real-time.
Mihaylov M, Jurado S, Avellana N, Van Moffaert K, de Abril IM, Nowé A. NRGcoin: Virtual currency for trading of renewable energy in smart grids. In 11th International conference on the European energy market (EEM14) 2014 May 28 (pp. 1-6). IEEE.
Video

## Slide 22
Sustainable Energy
Example: NRGCoin
Advantages
  Owning NRGCoin serves as a right to receive an equivalent quantity of energy in the future, independent of the NRGCoin market value. → increases prosumer’s revenue without the need for batteries. (Although batteries would also increase their profits)
  Unlike Bitcoin, which is mined through energy expenditure, NRGCoin is generated by injecting useful renewable energy to the grid.
Mihaylov M, Jurado S, Avellana N, Van Moffaert K, de Abril IM, Nowé A. NRGcoin: Virtual currency for trading of renewable energy in smart grids. In 11th International conference on the European energy market (EEM14) 2014 May 28 (pp. 1-6). IEEE.

## Slide 23
Blockchains for Sustainability
Emissions Trading
Sustainable Energy
Sustainable Mobility
Sustainable Supply-chain management
Example Use-Cases

## Slide 24
Sustainable Mobility
Machine-to-Human (M2H)
For example → Transportation-as-a-Service
M2X Economy

## Slide 25
Machine-to-Machine (M2M)
For example → Road space negotiations
Sustainable Mobility
M2X Economy

## Slide 26
Machine-to-Infrastructure (M2I)
For example → Smart parking, battery charging or traffic information
Sustainable Mobility
M2X Economy

## Slide 27
Machine-to-Human (M2H)
+
Machine-to-Machine (M2M)
+
Machine-to-Infrastructure (M2I)
=
Machine-to-Everything (M2X)
<number>
Sustainable Mobility
M2X Economy

## Slide 28
Blockchains for Sustainability
Example Use-Cases
Emissions Trading
Sustainable Energy
Sustainable Mobility
Sustainable Supply-chain management

## Slide 29
Sustainable Supply-chain management
In Theory
What if we could..
  Manage supply chain logistics using a public blockchain,
  With incentive structures for sustainable energy, reduction in emissions and waste production,
  Logistical infrastructure to enable circular economy practices.
Image adapted from https://www.ellenmacarthurfoundation.org/circular-economy/concept/infographic

## Slide 30
Sustainable Supply-chain management
In Literature
V. K. Manupati, Tobias Schoenherr, M. Ramkumar, Stephan M. Wagner, Sai Krishna Pabba & R. Inder Raj Singh (2019): A blockchain-based approach for a multi-echelon sustainable supply chain, International Journal of Production Research, DOI: 10.1080/00207543.2019.1683248

## Slide 31
Sustainable Supply-chain management
In Practice: Walmart + IBM Food Trust
Motivation: Food contamination traceability
  Heterogeneous record-keeping methods
  Supply chain participants know only the immediate supplier (one link up the chain) and the immediate customer (one link down the chain).
  Lack of accurate and adequate information leads to entire batches of food being thrown out in cases of food contamination.
Kamath, Reshma. 2018. “Food Traceability on Blockchain: Walmart’s Pork and Mango Pilots with IBM.” The Journal of The British Blockchain Association 1 (1). https://doi.org/10.31585/jbba-1-1-(10)2018.

## Slide 32
Sustainable Supply-chain management
In Practice: Walmart + IBM Food Trust
Implementation
  Permissioned blockchain developed in conjunction with IBM
  Based on Hyperledger Fabric
Proof of Concept (2016):
  Mangoes in the US → Reduced the time needed to trace provenence from 7 days to 2.2 seconds.
IBM Food Trust (2017)
  Walmart + IBM + Nestle + Unilever
Expansion to other products (2018)
  Walmart now traces 25 products from 5 suppliers.
    mangoes, strawberries and leafy greens, meat and dairy products, baby foods.
  Planned expansion to all leafy greens
“How Walmart brought Unprecedented transparency to the food supply chain with Hyperledger Fabric” - Link

## Slide 33
Blockchains for Sustainability
Quick reflection on the most valued properties
Which of the following properties of Blockchains would you value the most, when it comes to the potential utility for “making the world more sustainable / the economy more circular” ?
  Verifiability / Traceability / Transparency
  Decentralizing aspects (concensus)
  Immutability
  Security (e.g., preventing double-spending)
  (Psuedo-) Anonymity

## Slide 34
Blockchains for Sustainability
Technological barriers
Organizational barriers
Environmental barriers
  Inter-Organizational barriers
  External barriers
Disadvantages and Adoption barriers
Kouhizadeh, Mahtab, Sara Saberi, and Joseph Sarkis. "Blockchain technology and the sustainable supply chain: Theoretically exploring adoption barriers." International Journal of Production Economics 231 (2021): 107831.

## Slide 35
Blockchains for Sustainability
Technological Barriers
Transaction speed
Accumulating transaction costs
Scalability
Immutability
  Any private data going into a blockchain will stay there forever.
  Incorrect environmental or social record could exist forever, even though latest data seeks to correct such information.
Public Image and perceptions
Kouhizadeh, Mahtab, Sara Saberi, and Joseph Sarkis. "Blockchain technology and the sustainable supply chain: Theoretically exploring adoption barriers." International Journal of Production Economics 231 (2021): 107831.

## Slide 36
Blockchains for Sustainability
Financial constraints tied to developing a blockchain-based system
  Planning, development, deployment, management
Lack of knowledge and expertise
Lack of commitment from top or middle management
  Why would they invest in a new sustainable technology if it hurts their bottom line?
Organizational Barriers
Kouhizadeh, Mahtab, Sara Saberi, and Joseph Sarkis. "Blockchain technology and the sustainable supply chain: Theoretically exploring adoption barriers." International Journal of Production Economics 231 (2021): 107831.

## Slide 37
Blockchains for Sustainability
Inter-Organizational barriers
  “Organizations are skeptical about sharing their information as they see information as a competitive edge.”
  Cultural and geological differences: e.g., heterogeneous definitions of sustainability, circular economy, etc.
External barriers
  Lack of governmental incentives towards using blockchains for sustainability due to it’s bad public image.
  Novelty and instability of blockchains.
Environmental Barriers
Kouhizadeh, Mahtab, Sara Saberi, and Joseph Sarkis. "Blockchain technology and the sustainable supply chain: Theoretically exploring adoption barriers." International Journal of Production Economics 231 (2021): 107831.

## Slide 38
Blockchains for Sustainability
The more trust, verifiability and traceability you would like from a (public) blockchain, the more data you need to store.
Among others issues, this increases the risk of potential barriers to adoption.
This leads to alternative solutions like private/protected blockchains.
  → Little to no public verifiability: How can we know if a proposed solution is not greenwashing us?
A Contradictory Philosophy

## Slide 39
Blockchains for Sustainability
The more trust, verifiability and traceability you would like from a (public) blockchain, the more data you need to store.
Among others issues, this increases the risk of potential barriers to adoption.
This leads to alternative solutions like private/protected blockchains.
  → Little to no public verifiability: How can we know if a proposed solution is not greenwashing us?
Is there a better philosophy that works better ? / An alternative way to approach the problem of sustainability?
A Contradictory Philosophy

## Slide 40
A short detour: Circular SOCIETy

## Slide 41
Circular Society
Replace the LE with circularly oriented forms of consumption and production
CE focus mostly on earned value management: product/business model innovations within existing power asymmetries
Decouple economic growth and consumption of natural resources
→ But why do we need neverending economic growth and why is it good to consume as many goods and services as possible?
Alternatives:
Sufficiency strategies and lifestyle changes
Question the prevailing entrepreneurial orientation towards the shareholder concept
Deconstruction of existing power and hegemonic relations
CE Criticism
Partially based on: F. Hofmann, J. Zwiers (2018) – Circular Society – Eine pluralistische und emanzipatorische Alternative zur Circular Economy? – Link.
.

## Slide 42
Circular Society
Replace the LE with circularly oriented forms of consumption and production
CE focus mostly on earned value management: product/business model innovations within existing power asymmetries
Decouple economic growth and consumption of natural resources
→ But why do we need never ending economic growth and why is it good to consume as many goods and services as possible?
Alternatives:
Sufficiency strategies and lifestyle changes
Question the prevailing entrepreneurial orientation towards the shareholder concept
Deconstruction of existing power and hegemonic relations
CE Criticism
Partially based on: F. Hofmann, J. Zwiers (2018) – Circular Society – Eine pluralistische und emanzipatorische Alternative zur Circular Economy? – Link.
.

## Slide 43
Circular Society
Replace the LE with circularly oriented forms of consumption and production
CE focus mostly on earned value management: product/business model innovations within existing power asymmetries
Decouple economic growth and consumption of natural resources
→ But why do we need never ending economic growth and why is it good to consume as many goods and services as possible?
Alternatives:
  Sufficiency strategies and lifestyle changes
  Question the prevailing entrepreneurial orientation towards the shareholder concept
  Deconstruction of existing power asymmetries.
CE Criticism
Partially based on: F. Hofmann, J. Zwiers (2018) – Circular Society – Eine pluralistische und emanzipatorische Alternative zur Circular Economy? – Link.
.

## Slide 44
Circular Society
Circular Society → CS
Goals of the CS:
  Not just “CE + social”
  Socio-political transformation and reorganization
  Replace intransparent and inequity-based value chains of the LE with democratic, transparent and cooperatively organized value chains
Also → preserve the environment/ressources for present and future generations and enable social participation and quality of life
All-encompassing change necessary if the CE is to be the subject of a socio-ecological transformation
Democratisation of value creation processes and strategies for the activation and emancipation of different stakeholder groups
Overview
Partially based on: F. Hofmann, J. Zwiers (2018) – Circular Society – Eine pluralistische und emanzipatorische Alternative zur Circular Economy? – Link.
.

## Slide 45
Circular Society
Circular Society → CS
Goals of the CS:
  Not just “CE + social”
  Socio-political transformation and reorganization
  Replace intransparent and inequity-based value chains of the LE with democratic, transparent and cooperatively organized value chains
  Also → preserve the environment/resources for present and future generations and enable social participation and quality of life
All-encompassing change necessary if the CE is to be the subject of a socio-ecological transformation
Democratisation of value creation processes and strategies for the activation and emancipation of different stakeholder groups
Overview
Partially based on: F. Hofmann, J. Zwiers (2018) – Circular Society – Eine pluralistische und emanzipatorische Alternative zur Circular Economy? – Link.
.

## Slide 46
Circular Society
Circular Society → CS
Goals of the CS:
  Not just “CE + social”
  Socio-political transformation and reorganization
  Replace intransparent and inequity-based value chains of the LE with democratic, transparent and cooperatively organized value chains
  Also → preserve the environment/resources for present and future generations and enable social participation and quality of life
  All-encompassing change is necessary if the CE is to be the subject of a socio-ecological transformation
  Democratization of value creation processes and strategies for the activation and emancipation of different stakeholder groups
Overview
Partially based on: F. Hofmann, J. Zwiers (2018) – Circular Society – Eine pluralistische und emanzipatorische Alternative zur Circular Economy? – Link.
.

## Slide 47
Circular Society
„ A circular society defines discourses with a vision of circularity where not only resources are circulated in sustainable loops, but also wealth, knowledge, technology and power is
circulated and redistributed throughout society”
Definition
Image licensed under CC BY-SA 4.0, sourced from M. C. Friant, R. Salomone, W. J. V. Vermeulen (2020) – A Typology of Circular Economy Discourses: Navigating the Diverse Visions of a Contested Paradigm – Link

## Slide 48
Circular Economy (CE):
  Maintain natural resources and minimize the discharge of substances that are harmful to health and nature → Increase/maximize utilization of resources, e.g., Performance Economy
  Ecological modernization of the economy to increase resource efficiency, e.g., by technical innovation and digital solutions.
Circular Society (CS):
  Not just “CE + social” instead socio-political transformation and reorganization
  Replace non-transparent and inequity-based value chains of the LE with democratic, transparent and cooperatively organized value chains.
  Democratization of value creation processes and strategies for the activation and emancipation of different stakeholder groups
Circular Society
Conclusion

## Slide 49
Blockchains for Sustainability
The more trust, verifiability and traceability you would like from a (public) blockchain, the more data you need to store.
Among others issues, this increases the risk of potential barriers to adoption.
This leads to alternative solutions like private/protected blockchains.
  → Little to no public verifiability: How can we know if a proposed solution is not greenwashing us?
Is there a better philosophy that works better ? / An alternative way to approach the problem of sustainability? = Blockchains for Circular Societies?
A Contradictory Philosophy

## Slide 50
Blockchains for Circular Societies
Quick reflection on the most valued properties
Which of the following properties of Blockchains would you value the most, when it comes to the potential utility for “making the world more sustainable / the economy more circular” ?
  Verifiability / Traceability / Transparency
  Decentralizing aspects (concensus)
  Immutability
  Security (e.g., preventing double-spending)
  (Psuedo-) Anonymity

## Slide 51
Future work
Incentivise circular flows of material, energy, wealth, power, knowledge and technology.
Localized currency
  Incentivise local supply chains
  Resolving scalability issues
  Alleviating organizational and environmental barriers
Enable decentralized governing principles using smart contracts.
Can such a system co-exist, while simultaneously transforming the status quo?
Can individual localized circular societies interact (trade) with each other, expanding to a global level?
A Possibly Unexplored Research Area
How can blockchains help develop and reliably “sustain” circular societies?

## Slide 52
Conclusions
Possible utility of blockchains
  Emmissions Trading
  Sustainable Energy
  Sustainable Mobility
  Sustainable Supply-chain management
Most scientific literature agrees that blockchains can be a driving force to design circular economic business models.

## Slide 53
Conclusions
However, various adoption barriers prevent the most valued attributes of blockchains being used in an efficient manner.
  Organizational barriers
  Environmental barriers
Circular Economy VS Circular Society
  Replace intransparent and inequity-based value chains of the LE with democratic, transparent and cooperatively organized value chains
  Also → preserve the environment/resources for present and future generations and enable social participation and quality of life
  All-encompassing change is necessary if the CE is to be the subject of a socio-ecological transformation

## Slide 54
Conclusions
Blockchains can be the backbone of such transformational change
However, various adoption barriers prevent the most valued attributes of blockchains being used in an efficient manner.
  Organizational barriers
  Environmental barriers
Circular Economy VS Circular Society
  Replace intransparent and inequity-based value chains of the LE with democratic, transparent and cooperatively organized value chains
  Also → preserve the environment/resources for present and future generations and enable social participation and quality of life
  All-encompassing change is necessary if the CE is to be the subject of a socio-ecological transformation

## Slide 55
Questions?

## Slide 56
Additional Resources
Thalhammer, Felix, Pascal Schöttle, Matthias Janetschek, and Christian Ploder. "Blockchain Use Cases Against Climate Destruction." Cloud Computing and Data Science (2022): 22-38.
Kamath, Reshma. "Food traceability on blockchain: Walmart’s pork and mango pilots with IBM." The Journal of the British Blockchain Association 1, no. 1 (2018): 3712. Link
https://www.hyperledger.org/wp-content/uploads/2019/02/Hyperledger_CaseStudy_Walmart_Printable_V4.pdf
Kouhizadeh, Mahtab, Sara Saberi, and Joseph Sarkis. "Blockchain technology and the sustainable supply chain: Theoretically exploring adoption barriers." International Journal of Production Economics 231 (2021): 107831.