## Slide 1
Emerging Technologies for the Circular Economy
Lecture 5a: Internet of Things Communications
Prof. Dr. Benjamin Leiding
M.Sc. Anant Sujatanagarjuna
M.Sc. Shohreh Kia

## Slide 2
License
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License. To view a copy of this license, please refer to https://creativecommons.org/licenses/by-sa/4.0/ .
Updated versions of these slides will be available in our Github repository.

## Slide 3
Iot COMMUNICATIONS

## Slide 4
Overview

## Slide 5
Different ranges, different standards
Source: M.S. Mahmoud, A. Mohamad, “A Study of Efficient Power Consumption Wireless Communication Techniques/ Modules for Internet of Things (IoT) Applications”, January 2016, Advances in Internet of Things 06(02):19-29, DOI:10.4236/ait.2016.62002

## Slide 6
WPAN

## Slide 7
Wireless Personal Area Network
IP based
6LoWPAN (IPv6 over Low-Power Wireless Personal Area Networks)
IEEE 802.11p (V2V)
RuBee (IEEE standard 1902.1)
Not IP based
Bluetooth
ZigBee (IEEE 802.15.4-based)
IrDA (Infrared Data Association)
Z-Wave
And more.

## Slide 8
Bluetooth
Pros
Low power requirements
Resilient against interference
Cons
Low bandwidth
Limited range
Limited number of participants in network
Applications
Beacons
Fitness trackers, smart watches
Medical applications
Smart homes
Smart cars
Earbuds, headsets etc.
Classes for different applications with different ranges/power usages.

## Slide 9
Zigbee
Pros
Low power requirements
Scales to large network sizes (~6500 nodes)
Cons
Low range
Low bandwidth
Security issues (fixed, known fallback keys in at least one profile)
Applications
Wireless sensor networks (WSN)
Industrial automation
Smart homes

## Slide 10
6LoWPAN
Pros
IPv6 based
Built-in security
Scalability
Interoperability
Cons
Higher minimum requirements due to IPv6 minimum complexity
Not as popular as ZigBee
Applications
Wireless sensor networks (WSN)
Internet of Things
Industrial Internet of Things

## Slide 11
IEEE 802.11p
Vehicular network optimized
Vehicle to vehicle (V2V)
Vehicle to infrastructure (V2I) such as road side units (RSU)
Built in time synchronization
Applications
Vehicular networks

## Slide 12
WAN

## Slide 13
Wide Area Network
Service/subscription model based
Service provider runs infrastructure such as base stations and radio towers
Examples:
Cellular networks (UMTS/LTE/5G)
LoRa (Long Range, physical layer), LoRaWAN (MAC layer)
Sigfox

## Slide 14
Cellular network architecture
Grid of cell towers
Overlapping cells
Requires handover for mobile stations between cells
Network planning
Space division multiple access
Minimize interference
Avoid allocating overlapping spectrum on nearby cells

## Slide 15
5G
New radio communication techniques and spectrum
Support for device to device communications (D2D)
Improved performance
  Theoretical latency in single digit ms
  Bandwidth in gbps range
  Ability to provide connectivity in fast moving vehicles
  Enables more dense connectivity and scalability (more devices)

## Slide 16
LoRa/LoRaWAN
Uses unlicensed spectrum
Low number of base stations (Gateways) covers wide area
  7 are enough to cover Belgium
Only produced by a single company (Simtech)
High latency, no realtime applications
Subscription based
Misses some common features from LTE networks
  Only physical and MAC layers are covered => Higher OSI layers have to be implemented on top

## Slide 17
Sigfox
Uses unlicensed spectrum
Uplink
  100bps
  12B payloads
  Maximum of 6 messages per device and hour (140 per day)
Downlink
  600bps
  8B payloads
  Maximum of 4 messages per day
Open hardware
Network subscription based

## Slide 18
Router and gateways

## Slide 19
Router and Gateways
Router
Bridges two networks
Can translate between protocols
Routes data
Port forwarding and network address translation (mainly end user or carrier grade)
VNETs
Gateways (not in the routing sense)
Bridges wireless network and internet
Can translate between protocols
Edge/Fog computing capabilities (see next lecture)
Routers can be gateways

## Slide 20
Gateway example
Wireless sensor nodes running Contiki RPL with Ipv6
Node attached to gateway over USB acts as gateway
IPv6 connectivity between networks provided through SLIP (Serial Line Internet Protocol)

## Slide 21
Updated Exercise Schedule
15.04.2024 → Exercise 01 – Knowledge Test (MC)
22.04.2024 → Exercise 02 – Circular Economy (MC)
29.04.2024 → Exercise 03 – Lifecycle Assessment (LCA)
06.05.2024 → Exercise 04 – IoT Sensing and Gathering Data
13.05.2024 → Exercise 05 – IoT Data Processing
27.05.2024 → Exercise 06 – IoT Security
03.06.2024 → Exercise 07 – Industrial IoT
10.06.2024 → Exercise 08 – Blockchain (MC)
17.06.2024 → Exercise 09 – Blockchain Basics
24.06.2024 → Exercise 10 – Blockchain Conensus
01.07.2024 → Exercise 11 – Blockchain Tokens
The schedule of the exercises, IoT Data Processing & IoT Security, will be switched. The new order is as follows:

## Slide 22
Questions?